## Slide 1: Neural Network Approach to the Inverse Problem
Using feed forward and convolutional neural network to solve the inverse problem in EEG Source Localization

## Slide 2: Electroencephalogram
Cheap and efficient
High temporal resolution (around 6ms)
Information loss and low spatial resolution

## Slide 3: Source Localization
Methods that analyze the source of neural activity
Consists of the Forward Model and the Inverse model
Brain is split up into dipoles

## Slide 4: Source Localization: Forward Model
Simulation of data
Projection matrix
Noise

## Slide 5: Source Localization: Inverse Problem
Ill posed problem
Inverse projection matrix
Spread of neural activity
3D to 2D
Mostly mathematical

## Slide 6: Methodology
Forward Model → Data Generation
Inverse Model → Machine Learning Model
Data is split up in trials

## Slide 7: Machine Learning Model
There 108 electrodes present
Each dipole has a corresponding Standard Neural Network and Convolutional Neural Network

## Slide 8: Data Generation: State Determination
Each dipole is in one state during the whole trial
The states of the dipoles differ in their neural activity
There are 3 active (source) dipoles
There are n/2 noisy dipoles

## Slide 9: Data Generation: Neural Activity Simulation
Active: AR(1) process:
  The connectivity of each source dipole differs
Noisy: pink noise characterized by 1/f shaped power
Idle: no recorded dipole magnitude

## Slide 10: Data Generation: Projection
Noise ratio’s: Signal to noise (snr) & Channel Noise (cnr)
Projection matrix from Huang et al. (2016)

## Slide 11: Time Series Prediction
The data input is of size 108
  (electrodes)
The data output is of size 1
  (dipole magnitude)
Hyper parameters: Batch sizes, Adam optimizer, MSE, learning rate, nodes (1 hidden layer)

## Slide 12: Time Series Classification
The output is the state of the dipole
1 if active (source)
0 if noisy or idle
Hyper Parameters: Convolutional Nodes, Kernel Size, Stride, Dense Nodes, Batch size, Adam Optimizer, Log loss, learning rate

## Slide 13: Validation
Hyper parameters: Max validation fails, Validation frequency, minimum Validation performance increase

## Slide 14: Performance Measures
Prediction: Mean Squared Error
Classification: True Positive, True Negative, Dipole Accuracy
Dipole accuracy: choosing the correct three source dipoles

## Slide 15: Benchmark Models
eLoreta Model(Prediction & Classification):
  Iteratively minimizes weighted minimum norm equations
  Resolution matrix ()
  Spread function
Variance Model (Classification)

## Slide 16: Gridsearch
Trials: 1000
Timesteps: 100
Dipoles: 1000
Bayesian Tuning
Fixed set of dipoles
628 billion options

## Slide 17: Evaluation: Prediction
Research Questions:
  What is the difference between prediction of dipoles near the scalp and at the center
  Is there a difference when active sources are close to each other
  Are there significant differences between the outputs of the different neural networks
  Are the optimal hyper parameters similar for all neural networks
Benchmark:
  How does the model compare in terms of MSE performance

## Slide 18: Evaluation: Classification
Research Questions:
  How confident is the model
  How do noisy and idle time series differ
Benchmark models:
  Use the Variance model on both the prediction output of the eLORETA and the Machine Learning model
  Use the Machine Learning Classification model on the output of the eLORETA
  How does the model compare in terms of TN, TP and dipole accuracy

## Slide 19: Future Work & Discussion
Improving the prediction model by implementing an RNN
Using 1 CNN instead of n different ones
Training using a data set where each dipole occupies the active state
Using concepts of previous mathematical models

## Slide 20: Questions